2017/Feb./
http://www.kobe-kosen.ac.jp/~waseda/
Introduction of horizontal axis wind turbine rotation mechanism
(Beta Ver.ｘｘ)
Some fluid dynamics expression is barren of accuracy, because these files aims are for beginners.
About Creative Commons License
Wind Turbine Generator Paper Model by Kazuyoshi WASEDA is licensed under a Creative Commons 表示 - 継承 4.0 国際 License.
Refer to the production released in http://www.kobe-kosen.ac.jp/~waseda/wtgpapermodel/index-e.html
Check the following adress for the additional use of the files that is not permitted by the license. http://www.kobe-kosen.ac.jp/~waseda/wtgpapermodel/index-e.html

---
Contents
Variety of horizontal axis wind turbine
Foundation of Fluid dynamics and Airfoil element theory
Horizontal axis wind turbine rotation mechanism
What is Reynolds Number ?

---
Variety of horizontal axis
 wind turbine

---
Up wind type
-
Down wind type

---
Up wind type
Down wind type
Wind
Wind
Rotor blade located at front side of the tower
Rotor blade located at back side of the tower

---
Names of parts
Airfoil
Rotor Blade
Nacelle
Hub (root of the blade)
Spiner
Tower
Rotor Blade
Nacelle
Spinner
Airfoil
Hub
Tower

---
Horizontal axis wind turbine rotation mechanism

---
Before the wind turbine rotation mechanism,,,
Foundation of Fluid dynamics and Airfoil element theory
See　Wikipedia:
Misunderstandings about the generation of lift
Lift (force)
http://en.wikipedia.org/wiki/Bernoulli%27s_principle#Misunderstandings_about_the_generation_of_lift
http://en.wikipedia.org/wiki/Lift_%28force%29
More accurate information of fluid dynamics and the blade element theory
NASA:Incorrect Lift Theory 　http://www.grc.nasa.gov/WWW/k-12/airplane/wrong1.html
NASA:Incorrect Lift Theory #2 　http://www.grc.nasa.gov/WWW/k-12/airplane/wrong2.html
日本機械学会　流体工学部門：活動内容：楽しい流れの実験教室 　http://www.jsme-fed.org/experiment/
飛行機はなぜ飛ぶかのかまだ分からない?? - NPO法人 知的人材ネットワーク・あいんしゅたいん
http://jein.jp/jifs/scientific-topics/887-topic49.html

---
Lift and Drag
Lift: Normal force caused by flow
Drag: Parallel force caused by flow
L：Lift
Airfoil
Flow
D：Drag
Airfoil: The shape which maximize the lift and minimize the drag

---
It’s relatively same state!
Put an airfoil into the air flow = Move forward an airfoil in the (no flow) air
L：Lift
airfoil
Flow
D：Drag
Relatively same state
L：Lift
airfoil
No Flow
D：Drag
Move forward [airfoil]

---
Law of continuity (Flow rate)
Q[m3/s]=A[m2]V[m/s]＝constant
Q: flow rate[m3/s]
A：Cross section of flow [m2]
V：Flow velocity [m/s]
Pipe
Broad Small
wide Cross section narrow
A2
A1
Pipe
V2
Slow Flow velocity Fast
V1
Flow Rate Q[m3/s]=A1V1=A2V2=Constant

---
What’s happened at around the airfoil ?
=upper surface flow velocity is higher than lower surface
Narrow cross section
upper surface flow velocity is higher than lower surface
upper surface
Flow
lower surface

---
Bernoulli's principle
V：Flow velocity [m/s]
p：Pressure[Pa]
ρ：Density of the fluid [kg/m3]
Dynamic Pressure + Piezometric head = const.
Flow
See　Wikipedia:
Misunderstandings about the generation of lift
Lift (force)
http://en.wikipedia.org/wiki/Bernoulli%27s_principle#Misunderstandings_about_the_generation_of_lift
http://en.wikipedia.org/wiki/Lift_%28force%29

---
Bernoulli's principle
V1,V2：Flow velocity [m/s]
p1,p2：Pressure[Pa]
ρ：Density of the fluid [kg/m3]
p1>p2
Lift force
p2
p1
V2
V1
Flow
p1
p1
V1
V1
Airfoil upper surface shape >>> accelerate flow velocity >>> Low pressure >> Lift force
V1

---
Some fluid dynamics expression is barren of accuracy,,,
In any case, an airfoil is
the shape that regarded low drag force as high lift force

---
It is ideal to Keep the AoA which shows Largest Lift force-Drag force rate
What is Angle of Attack (AoA: a)
Large AoA gives not only high lift force(L) but also high drag force(D)
Larger AoA is trigger of the stall (separation flow)
It is ideal to Keep the AoA which shows Largest Lift-Drag rate (L/D or CL/CD)
CL: Lift Coefficient
CD: Drag Coefficient

---
It is ideal to Keep the AoA which shows Largest Lift force-Drag force rate
What is Angle of Attack (AoA: a)
Large AoA gives not only high lift force(L) but also high drag force(D)
Larger AoA is trigger of the stall (separation flow)
It is ideal to Keep the AoA which shows Largest Lift-Drag rate (L/D or CL/CD)
CL: Lift Coefficient
CD: Drag Coefficient

---
What is Angle of Attack (AoA: a)
The angle of attack is the angle between the chord line of an airfoil and the oncoming air.
AoA: a
Lift force
Flow
Drag force

---
It is ideal to Keep the AoA which shows Largest Lift force-Drag force rate
What is Angle of Attack (AoA: a)
Large AoA gives not only high lift force(L) but also high drag force(D)
Larger AoA is trigger of the stall (separation flow)
It is ideal to Keep the AoA which shows Largest Lift-Drag rate (L/D or CL/CD)
CL: Lift Coefficient
CD: Drag Coefficient

---
Large AoA gives not only high lift force(L) but also high drag force(D)
Large AoA
Large lift force
Flow
Large drag force too

---
It is ideal to Keep the AoA which shows Largest Lift force-Drag force rate
What is Angle of Attack (AoA: a)
Large AoA gives not only high lift force(L) but also high drag force(D)
Larger AoA is trigger of the stall (separation flow)
It is ideal to Keep the AoA which shows Largest Lift-Drag rate (L/D or CL/CD)
CL: Lift Coefficient
CD: Drag Coefficient

---
Larger AoA is trigger of the stall (separation flow )
Separation flow (airfoil performance is as same as simple flat panel)
Significantly decreases the lift force
Larger AoA
Stall
Flow
Significantly increases the drag force

---
It is ideal to Keep the AoA which shows Largest Lift-Drag rate (L/D or CL/CD)
[Carry out the performance test of airfoil in all AoA range]

---
Large AoA gives not only high lift force(L) but also high drag force(D)
Lift
CL: Lift Coefficient
CD: Drag Coefficient
Stall
Drag
0o
AoA:a

---
Glide ratio
[Lift-Drag rate] 　L/D[CL/CD]
L/D maximum
Stall
AoA which shows Largest Lift-Drag rate
0o
AoA:a

---
Horizontal axis wind turbine rotation mechanism

---
Horizontal axis wind turbine rotation mechanism
v=rw[m/s]
Blade plane of rotation
Using Microsoft Power Point animation function
Wind
W[m/s]
Apparent wind
V[m/s]
v=rw[m/s]

---
Horizontal axis wind turbine rotation mechanism
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]
Using Microsoft Power Point animation function
Drag
Lift
Rotation direction force by lift
Rotation direction force by drag(opposite direction)
The difference is
Actual
Rotation direction force

---
Altogether
"Large Lift-Drag rate" means "Wind turbine rotate"

---
Why the wind turbine blade is twisted?

---
Why the wind turbine blade is twisted?
There is velocity difference between at the root and the tip of the blade
r2
ω：angular velocity [rad/s]
r1
T:time
<
v1
The tip of the blade is higher in rotational speed than the root
v2

---
When it suppose to be
the central position of the blade
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
When it suppose to be
the tip of the blade
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
When it suppose to be
the root of the blade
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
The image of AoA from tip to root is…

---
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
If Blade is not twisted(straight),
        AoA is not optimized
 -> Optimized the AoA(a) for each blade position	=twist the blade
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s] at root
of the blade
Apparent wind
V[m/s]
at center position of the blade
Apparent wind
V[m/s]
at tip of the blade

---
Optimized the AoA(a) for each blade position
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
Optimized the AoA(a) for each blade position
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
Optimized the AoA(a) for each blade position
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
Optimized the AoA(a) for each blade position
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
Optimized the AoA(a) for each blade position
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
Optimized the AoA(a) for each blade position
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
Optimized the AoA(a) for each blade position
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
Optimized the AoA(a) for each blade position
=the wind turbine blade is twisted
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s] at root
of the blade
Apparent wind
V[m/s] at center position of the blade
Apparent wind
V[m/s] at tip of the blade
Actually, airfoil shape is different for each position of the blade, because of apparent wind velocity difference.

---
If the rotor blade rotation stopped…

---
If the rotor blade rotation stopped…
What it does?
v=rw[m/s]=0
Blade plane of rotation
Wind
W[m/s]

---
If the rotor blade rotation stopped…
What it does?
v=rw[m/s]=0
Blade plane of rotation
Wind
W[m/s]
　① Change the pitch angle
or…

---
If the rotor blade rotation stopped…
What it does?
Blade plane of rotation
② give more peripheral velocity[starting torque]
This slide is using Microsoft PowerPoint animation
Wind
W[m/s]
Apparent wind
V[m/s]
v=rw[m/s]

---
If the wind speed change?
Wind stops or gust of wind blew!

---
If the wind speed change?
If wind stops
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
If the wind speed change?
If wind stops
v=rw[m/s]
Wind
W[m/s]
Blade plane of rotation
Apparent wind
V[m/s]
AoA(a) get small => Lift will reduce

---
If the wind speed change?
If wind stops
v=rw[m/s]
Wind
W[m/s]
Blade plane of rotation
Apparent wind
V[m/s]
Change the angle[pitch angle]!
AoA(a) get small => Lift will reduce

---
If the wind speed change?
Windblast [gusty wind]
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]

---
If the wind speed change?
Windblast [gusty wind]
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Apparent wind
V[m/s]
AoA(a) get big => Lift will reduce [stall]

---
If the wind speed change?
Windblast [gusty wind]
v=rw[m/s]
Blade plane of rotation
Wind
W[m/s]
Change the angle[pitch angle]!
Apparent wind
V[m/s]
AoA(a) get big => Lift will reduce [stall]

---
If the wind speed change?
Always control the pitch angle
but
Wind turbine blade is heavy and pitch angle control is slower pace

---
Performance of wind turbine blade is not good for sensitive to AoA

---
Glide ratio
[Lift-Drag rate] 　L/D[CL/CD]
Max
If wind speed is changes=AoA changes
[See page 57-63]
Stall
0°
AoA[a]

---
Glide ratio[Lift-Drag rate] 　L/D[CL/CD]
Great performance but too much sensitive to AoA
Max performance is low but good performance at wide AoA range
Good performance for wind turbine blade
narrow AoA range
wide AoA range
0°
AoA[a]

---
What is Reynolds number?
What is Re?

---
Inertial forces
Viscous forces
 V : Apparent (wind) velocity [m/s]
 c:chord [m]
 n : The dynamic viscosity of the fluid (n=m/r 1.502x10−5 ) [m²/s]
 m : The kinematic viscosity of the fluid ([Pa·s], [N·s/m²] , [kg/(m·s)])
 r: The density of the fluid [kg/m³]　(1.203 kg/m³)
c:chord
The Reynolds number is,,,
-> Dimensionless quantity
-> The ratio of inertial forces to viscous forces within a fluid.
-> Used in the scaling of similar but different-sized flow situations, such as between an aircraft model in a wind tunnel and the full size version.
If Reynolds number is same
flow situation is same
Full size real car
Small model car

---
In the case of wind turbine
Real wind turbine
Small scale model wind turbine
Low velocity big size chord
High velocity small size chord
The dynamic viscosity of the air [same}
Real wind turbine
If Reynolds number is same
flow situation is same
Small scale wind turbine model in a wind tunnel